## Slide 1: 3D ICs: technology, system design challenges, solutions & benefits
Dragomir Milojevic

## Slide 2: Scaling is dead, long live the scaling!
sources: imec
Advanced patterning techniques (SADP, EUV, SAQP, …) enable Contact Gate Pitch (CGP) & Metal Pitch (MP) scaling
 0.5 area reduction node-to-node
power & performance scale too

## Slide 3
Moore’s law still on ?
Some reasons NOT to believe so (this is a short list …)
System design becoming more & more complex
  Routability becomes major challenge
Yield is (seriously) limiting the die size
  HPC dies are smaller and smaller
Scaling CGP & MP is becoming more & more expensive
  4th foundry abandons next gen CMOS (Aug. 2018)  Today only 3 remain in game (you can guess which ones …)

## Slide 4: Design complexity increases
CPP likely to stop @30nm  std cell height reduced to 7.5, 6 & 5Tracks
Cell height reduction causes pin density to increase at design-level
Higher pin-density aggravates congestion & design routability
7.5T
6T
5T
Standard cell (ND4D0)
160nm
192nm
240nm
7.5T
6T
5T
Low
High
Pin density
Design

## Slide 5: Area needs
Next gen system will be more parallel (more cores per CPU)
More cores mean more & deeper cache memories
We need more IC area on the top of CMOS scaling
Chart: Nº of cores (SPARC CPUs)
| 65nm | 40nm | 28nm | 20nm | 14nm | 10nm | 7nm | 5nm
Real | 8 | 8 | 16 | 32
Projected | 32 | 64 | 64 | 128
real / projected
T2
T3
T4
T5
M5
M6
M7
S7
kB /core
Nº of cores
Chart: Total on-chip cache per core
| 8 | 16 | 8 | 16
 | 536 | 408 | 641 | 672
 | 8321 | 4225 | 2272 | 2272
M5 (28nm) M6(28nm)  M7(20nm)  S7(20nm)
T2 (65nm)  T3(40nm)  T4(40nm)  T5(28nm)
L3
added

## Slide 6: Cost of advanced CMOS
More cores & more memory mean more connectivity (more wires)
Total wafer cost increases for advanced CMOS
BEOL cost doubles from 14 to 7nm
Chart: Nº of Metal Layers in BEOL stack Fujitsu SPARC CPU
| 130nm | 90nm | 65nm | 20nm | 10nm | 5nm
 | 8 | 10 | 11 | 13 | 15 | 17
real projected
Wafer cost breakdown
(relative to 14nm)

## Slide 7: 3D technology
Welcome to :

## Slide 8: Key 3D technology enablers
Through Silicon Vias (TSVs) – good Aspect Ratio (AR) is required for higher interconnect density and to keep wafer thin
  Minimum ø of 2µm (for min area overhead) & 40µm depth (complex to make)
Micro-bumps – bump flip-chip technology 40µm, significantly larger than 5µm øTSVs (don’t introduce area penalty like TSVs)
  To increase the inter-die connectivity density size needs to shrink to 10µm
Hybrid W2W bonding – Cu pads of 1.6µm pitch, could be 0.8µm (aggressive)

## Slide 9: Stacking flavors (die orientation)
Face-to-Back (F2B)
TSVs of the bottom die connect to the FEOL of the top die
TSVs & ubumps may not be aligned (presence of backside metal layers)
Not so dense 3D interconnect
Face-to-face (F2F)
Micro-bumps or Cu-pads, more dense 3D interconnect
Only two dies in the stack
Still need TSVs so get out (IO), but their numbers is small (<1k)

## Slide 10: Assembly level
Die-to-wafer (D2W)
One wafer processed & sliced
Single dies picked & placed on the top of another die at wafer level
Allows Known Good Die integration (test before stack)  increases yield, at the expense of stacking speed
Wafer-to-wafer (W2W)
Increased 3D stacked IC processing throughput
Lower 3D stack yield (because of compound defaults)
Typically smaller 3D pitch

## Slide 11: 3D tech overview

## Slide 12: 3D packaged system
Core layer
High performance FEOL
Complex BEOL
Possibly multiple dies
Dense memory layer
Upper cache layers and/or central memory (DRAMs)
Power Delivery Network
Back-side metal layers
uTSV directly to cells
Better IR drop & front side routing
Memory layer
SRAM cache (64MB to 1GB)
FEOL optimized for SRAM
Limited BEOL

## Slide 13: 3D system design challenges

## Slide 14: How to design 3D systems?
Die1
Floorplan
Die2
Floorplan
Die1
Die2
Std. synthesis
RTL
Single
netlist
3D P&R
3D PDK
2D PDK
Native 3D placement
Holy grail, disruptive & huge dev. effort (e.g. 3D clock tree synthesis)
It needs to be 3D pitch driven
Works for 3D stacking & sequential FEOL
Synthesis
Netlist
partitioner
Bot Die
netlist
Top Die
netlist
Partition
directive
Top Module
netlist
Die-by-Die flow
RTL
2D P&R
2D P&R
Can use existing 2D tools
How to supply partition directive ?
Manual – Logic/Memory-on-Logic
Automated – Logic-on-Logic
Work in progress
Available!
Work on sign-off

## Slide 15: Partitioning automation
Hierarchical clustering of gates after 2D P&R
Design transformed into graph:
  vertex – area of each gate-cluster
    Wiring inside intra-cluster wirelength; not compressible by 3D
  edge – inter-function connectivity (nº of wires)
    Wiring between vertexes  inter-cluster wirelength; potentially reduced by 3D
Graph can be partitioned to have 50-50% area split between the dies with:
  MinCut – minimizes inter-function connectivity
    Min number of 3D nets
  MaxCut – maximizes inter-function connectivity
    Max number of 3D nets
Die1
Die2
Die1
Die2

## Slide 16: Where to cut 2D system ?
Analysis of implemented 2D design (after P&R)
Relative histograms of Number of Wires & Wire Length (WL)
  X-axis uses Average Gate Pitch (AGP) to express WL (not absolute WL)
Observations
  More than 45% of wires are of length smaller than 5 AGP
  70% of WLtot is in range of 0.1k & 2k gates (this is where we should cut)
AGP=0.245um
a)
b)
70% of total WL

## Slide 17: Possible gains of 3D ?
Measure of system connectivity (C):
inter-cluster WL
total system WL
MinCut  C is low & constant across different cluster size (std. 2D placement tools use MinCut)
MaxCut  cluster size impacts C
a)
b)
c)
Inter-function wirelength significant for smaller functionalities
Up to 80% of total WL taken by inter-function WL (potentially cut by 3D)
For clusters from 0.1 to1Kgates inter-function WL is 55-75% of total WL

## Slide 18: Relation to 3D pitch
What about 3D nets count? Important since more 3D nets mean also finer 3D pitch
MaxCut generates up to 2 orders of magnitude more connections than MinCut (for the same design)
For MinCut & for smaller gate clusters no significant change
For MaxCut & smaller gate clusters  exponential rise in number of 3D connections
b)
a)
c)
To maximize benefits of 3D, system partitioning needs to be done with blocks of few hundreds gates resulting in many 3D pins
(i.e. we need fine 3D pitch & partitioning automation)

## Slide 19: Examples of benefits

## Slide 20: Demonstrators using die-by-die flow
Logic-on-Logic (no memory macros)
  Synthetic SoC – 16 Low Density Parity Check (LDPC) blocks
  Different connectivity to understand design impact on 3D gains
  Manual functional partitioning at RTL-level
    Possible in this case
Memory-on-Logic
  OpenSPARCT2 – 8 core MPSoC for HPC (open source version of commercial product)
  Looking at a single core
    22 memories for L1 & register file sub-system
  Automated netlist partitioning (generation of top/bottom & top-level netlists)
    Mandatory due to Nº of blocks and connectivity

## Slide 21: Logic-on-Logic SoC (16XLDPC)
a) Locally connected
Connectivity
Congestion
2D P&R
Full
connectivity
shown
b) Fully connected  more connectivity, more congestion, good for 3D
Partial
connectivity
shown

## Slide 22: 3D vs. 2D: WL & Area
3D design is compared with 2D with appropriate utilization to solve congestion (system routability)
Locally connected SoC  can’t benefit from 3D
Fully connected SoC  WL gains are in the range of 30%, depending on the 3D pitch
  1um  -34%
  2um  -23%
plus improved congestion allows die utilization increase in 3D resulting in area gains
  Total die area of 3D is -24% compared to 2D
a)
b)
c)
c)

## Slide 23: Memory-on-Logic: OpenSPARC core
Top (mem. die)
Bottom (logic die)
1.5um
b) Memory die first
Top (mem. die)
1.5um
Bottom (logic die)
Next die view flipped
a) Logic die first

## Slide 24: 2D vs. 3D WL distribution
Logic die first
3D saves from M4 and up (logic die)
   Total WL reduction: -20%
Limited use of BEOL for memory die
Memory die first is better
 3D betters 2D by -28%
Bottom Die First
a)
b)
Top Die First
c)
45% of critical path delay caused by wires Perf. improved by ~30%

## Slide 25: Summary & Conclusions

## Slide 26
2D CMOS scaling continues, but not smoothly …
3D integration technologies could extend the life of CMOS
  Complementary to device & standard cell scaling
  Better perf, power & area (better silicon utilization, less buffering)
  Fresh view of system integration (package-level integration)
Various flavors of functionally partitioned systems
  Memory-on-Logic – better performance & possible cost gains due to process optimization for memory layer
  Logic-on-Logic – for maximum performance benefits
Benefits tightly coupled to 3D technology parameters
  Fine 3D interconnect pitch is required to maximize benefits
Optimization space not yet fully deployed, full flow still missing
  Better clustering, partitioning methods etc.
  Across die timing optimizations, 3D clock tree synthesis etc.

## Slide 27
3D is not about research any more …
Thank you!